WANPIPE®

Load Balancing

with

NETGRAPH

Revision 1.0

Author: Alex Feldman

July 26, 2007

This manual covers the details how to configure Load Balancing for Sangoma cards using on netgraph(4).

## Assuming

- Wanpipe package 3.1.3 or later have been installed

- Your FreeBSD kernel has NETGRAPH enabled (please refer to FreeBSD Handbook for more details)

## Sangoma Wanpipe configuration

- Create WANPIPE configuration file using the ‘wancfg’ configurator

- Select Interface Operation mode: NETGRAPH

- Use as example bonding script sg_bond_if.sh from <wanpipe>/scripts directory in order to bond sangoma interfaces.

## How to run

- Run `wanrouter start` script to load all devices is used by load balancing solution.

- Bond specified interface by executing following command:

sh sg_bond_if.sh bond –p ng0 waga0 wbg0

This command will bond two interface waga0 and wbg0 together to new created netgraph interface ng0.

- Run sg_bond_if.sh script with setip parameter in order to set ip address for parent interface:

sh sg_bond_if.sh setip X.Y.Z.A X.Y.Z.B C.D.E.F

where:

X1.Y1.Z1.A – local ip

X2.Y2.Z2.B – remote ip

C.D.E.F - netmask

## References

- Netgraph (4) manual page

- All About Netgraph

- Configuring the FreeBSD kernel

- Call Sangoma Tech support:

Tel: 905.474.1990

Email: techdesk@sangoma.com