## Slide 1: Achieving optimal scalability and voice quality in open source telephony
Konrad Hammel
Software Engineer
Sangoma Technologies

## Slide 2: What is the Secret to scalability and quality?

## Slide 3: Using The best hardware and the best software

## Slide 4: Outline
Sangoma Hardware
  AFT-Series
  B-Series
  Other Hardware
Intro to Asterisk Architecture
Bottlenecks and Scalability Issues
  Everything in Software
  Chunk Size restriction of Dahdi
  Channel Based
  Monolithic Design
FreeTDM + SMG + SIP/Woomera
Questions???

## Slide 5: Sangoma Hardware

## Slide 6: AFT Series
Advanced Flexible Telephony
  Award winning design from scratch
OOP Design
  Modular -> PCI/PCIe interface, telephony interface, DSP
  Abstraction -> common base, Remora system
Higher per card cost but lower maintenance and easier to stock

## Slide 7: AFT Series - Continued

## Slide 8: AFT Series - Features
Octasic HWEC
  Industry’s 1st telco grade HWEC
  Adjustable 128ms tail
  Fully Independent…no fine tuning needed
  Fax/Modem and DTMF detection
Field Upgradable Firmware
  Fix bugs and add new features on the fly
Crash Proof Firmware
  Recover the card after “act of god” accidents
Industry first and only LIFETIME WARRANTY

## Slide 9: AFT Series - Features
Fax Sync
Reliable T1/E1/BRI to analog faxing
Syncs clock from digital to analog card
Remora Expansion System
Add more telephony ports without using PCI/PCIe slots
Up to 24 ports per card

## Slide 10: AFT Series - Analog
A200
  Low density modular
  2-24 port FXO/FXS
  2u, PCI/PCIe(E), half-length
  Optional HWEC (D)
A400
  High density modular
  2-24 port FXO/FXS
  2u, PCI/PCIe(E), full length
  Optional HWEC (D)

## Slide 11: AFT Series – Digital T1/E1
A10X line
  A101, A102, A104, and A108
2-8 T1/E1/J1 ports
Channelized for voice and data
2u, PCI/PCIe (E) half-length
Optional HWEC (D)

## Slide 12: AFT Series – Digital BRI
A500
2-6 port modular BRI, up to 24 with Remora
2u, PCI/PCIe (E), half-length
Optional HWEC (D)

## Slide 13: B-Series – Mix Mode
B700
Modular BRI and analog
2-4 BRI, 2 FXO/FXS
2u, PCI/PCIe(E) half-length
Optional HWEC (D)
5 year warranty

## Slide 14: B-Series – Mix Mode
B600
4 FXO ports, 1 FXS port
2u, PCI/PCIe, half-length
Optional HWEC (D)
5 year warranty
B601D
4 FXO, 1 FXS, 1 T1/E1/J1
2u PCI/PCIe , half-length
Comes with HWEC
5 year warranty

## Slide 15: Other Hardware
U100 (USBFXO)
2 port FXO interface via USB
Comes with HWEC
5 year warranty
UT-50/UT-51
Asterisk timing device
USB (UT-50) and internal pin header (UT-51) interface
5 year warranty

## Slide 16: Introduction to Asterisk Architecture

## Slide 17: Asterisk Architecture
Asterisk Core
Channel Drivers like Chan_SIP and Chan_Dahdi
Action Plan (dial plan)
Dahdi API
Hardware Drivers
Hardware
User Space
Kernel Space
Hardware (A10X, A200, B601, etc)
Wanpipe
Dahdi API
Chan_Dahdi
Asterisk Core
Dial plan
analog
HDLC
libPRI
SWEC
DTMF

## Slide 18: Bottlenecks and scalability issues

## Slide 19: Software Everything
HDLC encoding
  Easy but still takes processing power
  Very simple to do in FPGA based hardware
Echo Cancelling
  Extremely CPU intensive…complicated math
  Audio glitches when not perfect
  DSP designed to do math
DTMF Detection
  Like EC can be CPU intensive because it is math based
  Hardware EC DSP can easily take care of this

## Slide 20: Chunk Size
Dahdi takes 1ms = 8 bytes
  1000 interrupts per second!
  WHY???
    Analog signaling
    Software EC
    Software DSP
SOLUTION: Increase to 20ms chunks optimal for system performance (up to 70% less CPU load)
  How to Reduce Asterisk System load by 70%
Hardware/Wanpipe
A101 – 1 E1/PRI
Dahdi API
8 bytes
1ms
8 bytes
1ms
8 bytes
1ms
…..….

## Slide 21: Channel Based
PROBLEM: Channel Based API
  Each voice channel gets a kernel device
  Easy for user space…
  16 E1 ports = 496 devices
  HUGE amount of context switches
SOLUTIONS: Span Based API
  Each span gets a device
  A little more work in user space
  Much less work done in time dependent kernel

## Slide 22: Monolithic Design
PROBLEM: Dahdi, Chan_Dahdi, and Asterisk are linked directly
  If one fails, the whole system fails
  All load concentrate on one system
SOLUTION: Woomera or SIP
  Socket based connection to Asterisk
    A crash on one side does not kill the other side
  Client-Server Architecture
    Allows for 1-to-Many connections (load balancing)
    Asterisk registers into PSTN interface

## Slide 23: FreeTDM + SMG + Woomera/SIP

## Slide 24: FreeTDM + SMG + SIP
High Quality Sangoma Hardware
Wanpipe Kernel drivers
TDM API
FreeTDM + Sig stacks
SMG
Chan_SIP or Chan_Woomera
Asterisk Cores
User vs. Kernel Space
Sangoma Hardware
HW-HDLC, HWEC, HW-DTMF
Wanpipe
TDM API (20ms chunks)
FreeTDM
SMG
Asterisk
Chan _SIP
Asterisk
Chan _Woomera
PRI/BRI
SS7
analog

## Slide 25: Kernel Space
Sangoma Hardware
Telco grade quality
Hardware HDLC framing
Hardware Echo Canceling
Hardware DTMF Detection
TDM API
Small, Open Source, kernel based API
Runs at 20ms chunks
Can run in channel mode or span mode
No processing of any kind…just passes data
OS independent

## Slide 26: FreeTDM
Open Source, User space, C based TDM/PSTN API
Span based or Channel based
Unified..handles voice and signaling
  PRI, BRI, SS7, analog
  DTMF detection and generation
  Caller-id detection and generation
Complete hardware abstraction allows any hardware to run
“plug and play” stacks (open source and proprietary)
Operating system independent: Linux and Windows

## Slide 27: SMG
Sangoma Media Gateway
Open Source (always has been, always will be)
Connects to FreeTDM and uses the FS core to access SIP or Woomera , transcoding (HW or SW), logging (unified hardware, TDM, stack logging), and a web front end interface
Asterisk Channel bridging, SMG-to-SMG bridging
OS independent: Linux and Windows

## Slide 28: Conclusion
Voice quality in Asterisk can be improved by:
  Using telco grade hardware
  Using telco grade HWEC
  Optimizing for system load
Asterisk scalability is achieved by:
  Moving processor intensive tasks to hardware
  Reducing system load by increasing data chunk size
  Using a distributed architecture
Sangoma Hardware
HW-HDLC, HWEC, HW-DTMF
Wanpipe
TDM API (20ms chunks)
FreeTDM
SMG
Asterisk
Chan _SIP
Asterisk
Chan _Woomera
PRI/BRI
SS7
analog

## Slide 29: Questions?

## Slide 30: Thank you Come visit us at Booth A4