## Slide 1: Introduction to Asterisk Architecture
Konrad Hammel
Field Applications Engineer

## Slide 2: Architecture of a Soft PBX
Mile High view of a Soft PBX
Physical interface speaks to OS
Server App speaks to OS
Telephony Apps speak to Server App
Server app is the brain…it decides what goes where and when

## Slide 3: Asterisk Architecture
Asterisk is aware of “channels” and “applications that run on channels”
A channel is a single connection to any kind to any point
Asterisk can handle different kinds of channels because it uses translators called “channel drivers”
Asterisk applications run on channels after they have pasted through Asterisk

## Slide 4: Asterisk Architecture

## Slide 5: Asterisk Architecture
A Basic Call
  call goes from TDM hardware, through the drivers, abstraction API, and chan_zapata to Asterisk
  Asterisk then routes the call to the dial plan where Asterisk is told which Application to use
  Asterisk uses the Dial application to setup another channel using chan_sip.
  Chan_sip then sends the call to a SIP via the NIC

## Slide 6: Key Asterisk Files
Extensions.conf
  This is the dial plan…tells asterisk what to do with a call
Zapata.conf
  Chan_zapata configuration file
Sip.conf
  Chan_sip configuration file
Woomera.conf
  Chan_woomera configuration file
Logger.conf
  Controls the Asterisk logging utilities, very important for debugging
Modules.conf
  Controls which channel drivers Asterisk does or does not load.

## Slide 7: Key Asterisk Commands
From the Linux CLI
  Asterisk
    Starts asterisk
  Asterisk –r
    Connects to the asterisk console
  Asterisk –rx “help”
    Runs the command inside of the quotes in the Asterisk CLI and displays the output in the Linux CLI
From the Asterisk CLI
  Help
    Displays all the commands Asterisk knows at that time
  Core show channels
    Shows all active channels
  Stop now
    Asterisk shuts down right away
  Exit
    Exits out of the Asterisk CLI

## Slide 8: Key Asterisk Directory
/etc/asterisk/
  Location of Asterisk config files
/var/log/asterisk/
  Location of Asterisk log files
/var/spool/asterisk/outgoing/
  Location of Asterisk call files
/var/lib/asterisk/sounds/
  Location of Asterisk sound files
/usr/lib/asterisk/modules
  Location of Asterisk applications, modules, etc

## Slide 9: Scaling Asterisk TDM Architecture

## Slide 10: Outline
Why do we need to scale?
Zaptel/Asterisk Architecture review
Short comings of this design and how they can be overcome
  Zaptel does ALOT (maybe to much?)
  TDM Hardware Restrictions
  Singular System Design
Sangoma’s Suggested Solution
  TDM Voice API + Sangoma Media Gateway + Chan_Woomera

## Slide 11: Zaptel/Asterisk Architecture
Zaptel API abstracts TDM hardware from User space
Signalling channels go to a signalling stack
Audio channels go to Asterisk Channel driver
Zaptel takes care of DTMF, HDLC framing, Echo cancelling, voice processing, etc

## Slide 12: Zaptel Does A LOT…
Zaptel by default does:
  Echo cancelling
  HDLC framing
  DTMF Detection/Generation
Why…?
Solution? Move it all to the hardware card:
  Hardware Echo cancelling
  Hardware HDLC Framing
  Hardware DTMF detection
FPGAs and DSPs are cheap and efficient

## Slide 13: TDM Hardware Restrictions Cont’d
Zaptel takes 1ms of data from each span at a time
Good for 1 or 2 ports but:
  8 ports = 8000/sec
  16 ports = 16000/sec
  32 ports = 32000/sec!!!
Solution:
  Design better hardware buffers so that 1 interrupt can service an entire card
  Increase the Zaptel Chunk size (8, 16, 40, or 80 bytes)
./Setup install –zaptel-chunk=

## Slide 14: Singular System Design
Zaptel and Chan Zap designed to run on same system as Asterisk
What about:
  Distributed computing
  Clustering
  Redundancy
Solution:
  Redesign Zaptel and Chan Zap so that they can be run on different systems
Again major redesign of Zaptel and Chan Zap needed

## Slide 15: Sangoma’s Solution: Stage 1
Zaptel is replaced with TDM Voice API
Chan Zap is replaced with SMG and Chan_Woomera
Sangoma Media Gateway
  Has access to “Boost” signalling stacks
  DTMF generation, Caller-id, etc
  Woomera Server
Chan_Woomera
  Socket based communication to Woomera server
  Text based call signalling
  Ulaw or Alaw

## Slide 16: Sangoma’s Solution: Stage 2
Chan_Woomera allows:
  Distributed computing
  Load balancing
TDM Voice API is replaced with the High Performance TDM Voice API
  Data is passed up a span at a time
  SMG decodes the span into channels
Currently being tested in our labs with 32 E1s

## Slide 17: Sangoma’s Solution: Stage 3

## Slide 18: Thank you. Konrad Hammel