## Slide 1: Introduction to Wanpipe
Konrad Hammel
Field Applications Engineer

## Slide 2: What is Wanpipe?
Sangoma’s Suite of hardware drivers
Set of utilities to configure, start, stop, and manage Sangoma hardware
  Wancfg
  Wanrouter
  wanpipemon
Voice and Data APIs
Documentation for drivers, utilities and APIs
Sample configuration files

## Slide 3: Commands

## Slide 4: wancfg
Utility to create configuration files for the various Sangoma cards
Each mode of operation as it’s own variation
  Zaptel mode (TDM Voice) -> wancfg_zaptel
  SMG Mode -> wancfg_smg
  TDM Voice API -> wancfg_tdmapi
  Data routing -> wancfg

## Slide 5: wanrouter
“wanrouter start/stop/restart”
  Starts, stops, and restarts all configured ports by loading the correct kernel modules and then applying the configuration for each port
“wanrouter hwprobe”
  Shows all Sangoma cards installed in the system and recognized by the current Wanpipe drivers
“wanrouter hwprobe verbose”
  A more detailed view of the Sangoma hardware installed including FXO/FXS modules, BRI modules, and LIU model number
“wanrouter status”
  Shows the state of all running ports.
“wanrouter version”
  Shows the version of the currently installed driver

## Slide 6: wanpipemon
“wanpipemon –p aft”
  Display all the possible command variation for AFT cards
“wanpipemon –g”
  Graphical version of the command
“wanpipemon –I w1g1 –c Ta”
  Show the line alarms for a T1/E1/J1 port
“wanpipemon –I w1g1 –c tr”
  Show a raw line trace for the interface
“wanpipemon –I w1g1 –c astats –m 1”
  Show the voltage on analog module 1

## Slide 7: Files

## Slide 8: Configuration Files
All configuration files are kept at /etc/wanpipe/
Important files and sub-directories:
  Wanrouter.rc
    Global configuration options. i.e. order in which the ports will be started in
  wanpipeX.conf
    Configuration file for a port/card
  Smg_bri.conf
    BRI configuration file for SMG
  scripts/
    Can contain a “start” and “stop” script that will be run after starting and before stopping the ports
  Api/
    Location of API documentation and sample applications
  Util/wan_aftup/
    Firmware update utility

## Slide 9: wanpipeX.conf
One file for each:
  A10X, A14X port
  A200/A400/A500/B600/B700 card
  USB-FXO device
File consists of 4 sections:
  Device definition
  Interface definition
  Global device options
  Interface specific options
http://wiki.sangoma.com/Wanpipe-Asterisk-Configuration-File

## Slide 10: Installing Wanpipe

## Slide 11: Installing Wanpipe
Very easy…just run the “Setup” script
Download the latest beta or stable from wiki.sangoma.com to /usr/src/
Untar the source files
Enter the newly created directory
Start the install script “Setup”
Answer “Yes” or the default to all questions
Select your mode of operation
Answer “Yes” or the default to all questions

## Slide 12: Thank you. Konrad Hammel