## Slide 1: Introduction to PSTN Lines
Konrad Hammel
Field Applications Engineer

## Slide 2: Outline
Difference between an E1 line and an PRI line
Types of lines:
  POTS, T1, and E1
Signalling Protocols:
  FXS, FXO, CAS, CCS, ISDN
Echo

## Slide 3: E1/T1 vs PRI
Apples and oranges
Line protocol vs call signaling
Not interchangeable

## Slide 4: POTS Lines

## Slide 5: POTS Lines
Oldest telephone lines…this is where it all started
Usually 2 copper wires, sometimes 4
analog or digital signals can be transmitted
Prone to noise because there is no shielding
  Twisted pairs if the line is new

## Slide 6: T1/E1 Lines

## Slide 7: T1 Lines
DS1…Digital Signal 1
Continuous stream of digital data
Consists of 24 “channels” called DS0s
  DS0 is a 64kbps channel
  Each channel is multiplexed 8 bits at a time
Total Bandwidth of 1.544Mbps
Two types of coding:
  AMI -> Alternate Mark Inversion
  B8ZS -> Bipolar with eight-zero substitution
Two types of framing:
  SF -> Super Framing or D4
  ESF -> Extended Super Framing or D5

## Slide 8: E1 Line
Same theory as a T1 but:
  31 DS0s + 1 DS0
  Total Bandwidth of 2.048Mbps
Line coding:
  HDB3 -> high density bipolar of order 3
Line framing:
  CRC4 or NCRC4

## Slide 9: CAS vs CCS
Not actually a protocol but rather a theory
Theory that dictates the framing and coding
Channel Associated Signaling
  Each channel has 4 bits used to signal calls
Common Channel Signaling
  One channel is reserved for call signaling

## Slide 10: FXO/FXS

## Slide 11: Analog Call Signaling
Original method to signal a call…why mess with what works?
FXO
  Foreign Exchange Office
  Slave of the link
  Signals events by closing or opening the loop
FXS
  Foreign Exchange Station
  Master of the link
  Generates signaling voltages, dial tones, and ringing

## Slide 12: ISDN

## Slide 13: ISDN
Most common call signaling method
Uses one channel to send a digital call signaling
D-channel=signaling, B-channel=voice
1 D-channel can control many B-channels (NFAS -> Non-Facility Associated Signaling)
D-channels use 2 protocols to send messages:
  Q.921
  Q.931
ISDN is divided into 2 sub-protocols for physical line transmission; PRI and BRI.

## Slide 14: ISDN Cont’d
PRI
Primary Rate Interface
Uses T1 or E1 lines
Uses an RJ48c
Point to point
BRI
Basic Rate
Has 2 B-channels and 1-D channel
Uses RJ45 connector but has special pinout
Point to point and point to Multi-point

## Slide 15: ECHO

## Slide 16: Echo
Your audio stream reflected back to you
TX recorded and compared to RX
Delays of 16ms+ are picked up by the human ear
3 main sources of echo
  Compression
    G.729 = ~15ms
  Distance
    Copper lines = ~1ms per 100 miles
  Transcoding (TDM to IP)
    Buffering = ~5-50ms

## Slide 17: Other Types of Echo
Acoustic Echo
Hybrid Echo
  4 wires down to 2 wires

## Slide 18: Thank you. Konrad Hammel