NEWS RELEASE

Contacts:

Sheldon Rose

Sacke & Associates Inc.

416.493.5723, ext. 202

sheldonr@sackepr.com

SANGOMA TECHNOLOGIES NOW SHIPPING LATEST

# A400 FXO/FXS ANALOG TELEPHONY SUPPORT SYSTEM

The A400 and REMORA system support up to 48 FXO/FXS ports

TORONTO, ON – November 30, 2006  – Sangoma Technologies Corporation (TSXV: STC) (www.sangoma.com), a leading provider of connectivity hardware and software products for VoIP, TDM voice, WANs and Internet infrastructure, is now shipping its A400 Series --  the high density version of the popular A200 series analog cards.

Identical in operation and configuration and using the same FXO and FXS modules, the A400 system supports twelve ports per main board and REMORA, as compared to four ports for the A200.

“As you need them, additional REMORA cards can be added to the base 12-port A400 card,” says Sangoma Technologies president and CEO David Mandelstam.  “A single PCI or PCI Express slot host connection can support up to 48 FXO/FXS ports with common synchronous clocking for all channels.”

Like all the Sangoma AFT Series, the A400 and REMORA system has field upgradeable firmware to take advantage of enhancements as they become available. Optionally, the A400 supports Sangoma's echo cancellation and voice enhancement DSP daughterboard for carrier grade echo cancellation and voice enhancement.

Since launching the A200 earlier this year, we continue to see a huge demand for analog telephone connections in many countries around the world,” adds Mandelstam.  “VoIP telephony with all its promise still needs access to the existing PSTN network and many of those connections are analog FXO or FXS. To meet this requirement we are taking an industry lead by providing a price/performance solution that our competitors will now attempt to follow.”

The A400 consists of an A400 REMORA daughterboard mounted on the AFT PCI /PCI Express. Each A400 REMORA card can support up to 12 FXO or FXS connections.

Up to three additional A400 REMORA daughterboards can be mounted in empty slot positions beside the A400 assembly, connected to the A400 by a backplane bus connector.

Each 12 port A400 REMORA card is connected by means of a standard 12-line color coded telephone cable terminating at the card in a robust DB25 connector, and ready for hard wiring into a punch block at for the PSTN connection.

-30-

About Sangoma Technologies Corporation

Founded in 1984, Sangoma develops and manufactures wide area network (WAN) communication hardware and software products, with an emphasis on the PC platform. The communications solutions, voice, data and video gateways support all popular WAN networks, line protocols and all standard PC operating systems and platforms including Linux, Windows, FreeBSD and Sun Solaris. Sangoma Technologies Corporation is publicly traded on the TSX Venture Exchange (TSXV: STC - News).

###

Technical Specifications

- From 2 to 48 ports supported, mixing FXO and FXS interfaces as required

- Support for the Asterisk™, Yate™, FreeSwitch™ OPAL™ PBX/IVR projects, as well as other Open Source and proprietary PBX/Switch/IVR/VoIP gateway applications

- Single synchronous PCI interface up to 48 FXO/FXS ports

- Connection by means of a standard 2 line colour coded telephone cable for connection to a punch block

- Dimensions: 2U height form factor: 290mm x 55 mm foruse in a 2U chassis. Short 2U compatible mounting clips available for installation in 2U rackmount servers

- 32 bit bus master DMA data exchanges across PCI interface at 132Mbytes/sec for minimum host processor intervention

- Autosense compatibility with 5v and 3.3v PCI busses

- Fully PCI 2.2 compliant, compatible with all commercially available motherboards, proper interrupts sharing

- Intelligent hardware: Downloadable Field Programmable Gate Array programming with multiple operating modes. Field upgradeable so that new features related to voice and/or data can be added when they become available

- Power: 800mA peak, operational 300mA max at +3.3v or 5v

- Temperature range: 0 - 50C

## Optional DSP daughterboard on the A400d

- G.168-2002 echo cancellation in hardware

- 1024 taps/128ms tail per channel on all channel densities

- DTMF decoding and tone recognition

- Voice quality enhancement: Octasic music protection, acoustic echo control and adaptive noise reduction.